## Slide 1
ISE 5264 Assignment 1
Due: November 5, 2024

## Slide 2
Overview
The purpose of this assignment is to enable the students learn the basics of applying a simulation modeling technique to a real-world semiconductor manufacturing process, where efficient coordination between machines and material handling systems is critical.
This assignment is divided into various sections focusing on different features of a simulation model. The features discussed in each of the sections are to be implemented in the same fab layout discussed next.
The slide deck is organized as follows:
      Problem Description
      Layout designs
      Machine Failures
      Stochasticity

## Slide 3
Problem description

## Slide 4
1
2
3
Pt 2
Pt 1
Pt 3
75
70
20
20
20
Pt1 | Parking spot 1
Pt2 | Parking spot 2
Pt3 | Parking spot 3
1 | Diffusion
2 | Lithography
3 | Implantation
Wafer fab layout
20
20
20
20
20
Stations
Pt
Parking Spots
30
30
Job Enters
Job Exits
Direction of vehicle movement

## Slide 5
Problem Description
      The above figure presents a layout of the wafer fab company XYZ. The Company produces a single product, which uses a re-entrant type of flow for its fabrication. It requires a total of 6 fabrication steps. These steps are carried out at three different stations, namely, diffusion, lithography and implantation. The details of these fabrication steps are given in the following table.
      The number of machines of each type available at various stations is given in the table below:
Step No | Station used | Usage time (in mins)
1 | 1 | 225
2 | 2 | 30
3 | 3 | 55
4 | 2 | 50
5 | 1 | 255
6 | 3 | 10
Station no | Process Name | No of Machines
1 | Diffusion | 2
2 | Litho | 2
3 | Implantation | 1

## Slide 6
Layout Design

## Slide 7
Key Learnings
How to design a layout using AutoMod.
How to utilize resources, queues, vehicles, worklists, and park lists.
Syntax of AutoMod, and development of a code using AutoMod.
Calculating Makespan in AutoMod.
Determining optimal parking spot for vehicles in a given layout.

## Slide 8
Questions
A total of 10 wafers are processed in the XYZ Fab. All 10 wafers undergo the same process flow.
Determine the makespan when the parking spot of the vehicle is set at Pt1, Pt2 or P3.
Which parking spot or a combination of two parking spots gives the best makespan?
Which station is the bottleneck? Also, give the utilization of the bottleneck station.
Given your answer to Q.2 above, what will be the makespan if the number of machines at the Diffusion station is increased by 1 unit?
Given your answer to Q.2 above, what will be the makespan if the number of machines at the Implantation station is increased by 1 unit?
Given your answer to Q.2 above, what will be the makespan if the number of machines at the Lithography station is increased by 1 unit?

## Slide 9
Machine Failures

## Slide 10
Key Learnings
Deterministic variability in uptime and downtime.
How to add the features of MTTF and MTTR for resources in AutoMod.
How do changes in MTTF and MTTR impact makespan.
Identifying dominance between MTTR and MTTF in impacting makespan.
Understanding the impact of the MTTF/MTTR ratio on makespan.

## Slide 11
Questions
A total of 1000 wafers are processed in the XYZ Fab. All 1000 wafers undergo the same process flow.
[A] All 1000 wafers are available at the start of the simulation.
What is the makespan?
Suppose the machines undergo periodic failures, and the Mean Time to Failure (MTTF) is 50 hours and the Mean Time to Repair (MTTR) is 50 hours for each machine at each station. What is the makespan now?
Assume the machines undergo periodic failures. Fill in the following table and plot graphs to reveal trends in makespan variation for various combinations of MTTR and MTTF. Also, plot graphs of makespan variation if MTTF in increased keeping MTTR constant, and then, if MTTR in increased keeping MTTF constant? Which variation is more dominant in impacting the makespan?
Does the makespan depend only on the ratio MTTF/MTTR or do the individual values of MTTF and MTTR play a roll as well? To investigate this, calculate makespans for various values of MTTF and MTTF when the ratio MTTF/MTTR equals 1 and 2. What inference can you draw from these results?
 | MTTF | 10 | 20 | 30 | 40 | 50
MTTR |  |  |  |  |  | 
10 |  |  |  |  |  | 
20 |  |  |  |  |  | 
30 |  |  |  |  |  | 
40 |  |  |  |  |  | 
50 |  |  |  |  |  | 

## Slide 12
Stochasticity

## Slide 13
Key Learnings
Impact of the stochasticity present in the form of variability in different parameters such as wafer arrival rate, MTTF, MTTR, and processing times.
Variation in which of the MTTF and MTTR has the greatest impact on makespan?
Variation in which of the MTTF, MTTR, processing times, and arrival rate has the greatest impact on makespan?
How combined variability affects makespan?

## Slide 14
Questions
[B] A total 1000 wafers are processed in the XYZ Fab. All 1000 wafers undergo the same process flow. The wafer start rate is 1 wafer every 0.5 hours. Also, the mean values of the MTTF and MTTR are 50 hours for all the machines.
Determine the makespan.
2. Now, assume the MTTF to be a random variable, which is normally distributed. Determine the makespan if the standard deviation is the following percentage of the mean:
            0%
            20%
            30%
3. . Next, assume the MTTR to be a random variable, which is normally distributed. Determine the makespan if the standard deviation is the following percentage of the mean:
            0%
            20%
            30%
4. . Next, assume both MTTF and MTTR to be random variables, which are normally distributed. Determine the makespan if their standard deviations are the following percentages of the mean:
            0%
            20%
            30%
5. Now, consider variability in wafer arrival. Suppose the wafer arrival is normally distributed with the mean of 0.5 hours. Determine the makespan if the standard deviation is the following percentage of the mean:
            20%
            30%
6. Next, consider variability in the processing times at all the stations, which are normally distributed with mean equal to their deterministic processing time values. Determine the makespan if the standard deviation of each processing time is the following percentage of the mean:
            20%
            30%